## Slide 1
By Khushal

## Slide 2
Introduction
The Raspberry Pi is a low cost, credit-card sized computer.
It plugs into a computer monitor or TV, and uses a standard keyboard and mouse.
Its use to explore computing, and to learn how to program in languages like Scratch and Python.
Its avaiable with either 1, 2 and 4 GB RAM.

## Slide 3
GPIO Pins

## Slide 4
GPIO Pins

## Slide 5
GPIO Pins
28x user GPIO supporting various interface options:
  Up to 6x UART
  Up to 6x I2C
  Up to 5x SPI
  1x SDIO interface
  1x DPI (Display Parallel Interface)
  1x PCM
  Up to 2x PWM channels
  Up to 3x GPCLK outputs

## Slide 6
GPIO Pins
GPIO pins can be switched (multiplexed) into various other modes backed by dedicated peripheral blocks such as I2C, UART and SPI.
Wirinig PI provide functionality for convenient programming for program in C.
  pinMode(PIN_nr, OUTPUT); //Set direction O/P
  pinMode(PIN_nr, INPUT); //Set direction I/P
  digitalWrite(PIN_nr, HIGH); // Set Pin
  digitalWrite(PIN_nr, LOW); // Clear Pin
  digitalRead(PIN_nr); // Read pin

## Slide 7
GPIO Pins
#include <wiringPi.h>
int main (void)
{
wiringPiSetup () ;
pinMode (3, OUTPUT) ;
for (;;)
{
digitalWrite (3, HIGH) ; delay (500) ;
digitalWrite (3, LOW) ; delay (500) ;
}return 0 ;
}
$ gcc -Wall -o buttons buttons.c -lwiringPi

## Slide 8
GPIO Pins
Interrupt can be set using GPIO pins by using:
wiringPiISR(button, INT_EDGE_FALLING, &myInterrupt);
Here,
Button = GPIO_pin_number
EDGE = Rising or Falling
MyInterrupt = ISR

## Slide 9
GPIO Pins

## Slide 10
GPIO Pins
#include <linux/gpio.h> // Header file
int gpio_request(unsigned int gpio, const char *label);
void gpio_free(unsigned int gpio); // Free requested GPIO
int gpio_direction_input(unsigned int gpio); // Set for sensor
int gpio_direction_output(unsigned int gpio, int value);
void gpio_set_value(unsigned int gpio, int value);
int gpio_get_value(unsigned int gpio); // Read GPIO

## Slide 11
Thanks...